## Slide 1: Implementation of Image Encryption and Decryption in Verilog
UEC1811-PROJECT WORK
Domain – Very Large Scale Integration(VLSI)
GUIDED BY
Mr. R. Balamurugan ME.,(Ph.D),
Assistant professor,
Department of ECE,
K.Ramakrishnan College Of Engineering.
TEAM MEMBERS
Narmatha M – 8115U20EC063
Nisha V R - 8115U20EC067
Pooja R - 8115U20EC070
DEPARTMENT OF ECE

## Slide 2
CONTENTS
ABSTRACT
INTRODUCTION
LITERATURE SURVEY
EXISTING SYSTEM
CHALLENGES IN EXISTING SYSTEM
PROPOSED SYSTEM
SOFTWARE REQUIREMENT
MODULE DESCRIPTION
CONCLUSION
FUTURE SCOPE
REFERENCES

## Slide 3
ABSTRACT
In this project, proposes an image encryption and decryption modules based on the Advanced Encryption Standard (AES) and Data Encryption Standard (DES) algorithms in128-bit keys using Python and Xilinx.
Block cipher modes of operation such as Electronic Codebook (ECB), Cipher Block Chaining (CBC), Cipher Feedback (CFB), and Output Feedback (OFB) to improve security and enable the encryption of arbitrary-sized images.
In order to improve data security and optimize the rate of time we created verilog code to implement 128 bits of AES and DES for image encryption and decryption that is synthesized and simulated USING XILINX TOOL. We achieved the Maximum Frequency 100MHz and the power consumption rate is 28007.343nw

## Slide 4: INTRODUCTION
Encryption
Encryption is the process of converting readable data (plaintext) into an unreadable format (ciphertext) using a cryptographic key.
This ensures that only authorized parties with the correct key can decode the ciphertext back into plaintext, protecting the information from unauthorized access.
Decryption
Decryption is the process of converting encrypted data (ciphertext) back into its original form (plaintext) using a secret key or password.
It ensures that only authorized users can access the information, protecting it from unauthorized access and maintaining privacy during data transmission.

## Slide 5
Block diagram for encryption and decryption

## Slide 6
MAIN TYPES OF ENCRYPTION METHEDOLOGIES
There are 2 main types of encryption methodologies:
Symmetric Encryption
In symmetric encryption, the same secret key is used for both encryption and decryption,
shared between the sender and receiver. It must remain confidential for security.
This method is faster and more efficient than asymmetric encryption.
Common symmetric algorithms include AES and DES.
Asymmetric Encryption
In asymmetric encryption, or public-key encryption, a public key is used for encryption and a private key for decryption. The public key can be freely distributed, enabling anyone to encrypt data that only the private key holder can decrypt.
It is slower but offers additional security benefits like secure key distribution and non-repudiation. Common asymmetric encryption algorithms include RSA and ECC.

## Slide 7
AES (Advanced Encryption Standard)
AES is a widely used symmetric encryption algorithm that supports key lengths of 128, 192, and 256 bits.
It is commonly used in various applications, including secure communication, data storage and encrypt of sensitive information.

## Slide 8
DES is a symmetric-key block cipher that encrypts data in 64-bit blocks using a 56-bit key.
It uses a Feistel network structure with multiple rounds of encryption and a complex key schedule. Despite its historical significance, DES is now considered insecure for practical use due to its small key size.
DES (Data Encryption Standard)

## Slide 9
S.NO | JOURNAL TITLE | AUTHORS | YEAR | DISCUSSIONS
1 | AES Based Algorithm for Image Encryption and Decryption | Prof. Venkatesha G Dr. Dinesh S Dr. Manjunath M | 2020 | The paper implements AES for image encryption, focusing on secure data transmission. 2. It describes the AES 128-bit Verilog synthesis on FPGA, showcasing its efficiency in encryption.
2 | Image Encryption and Decryption using AES Algorithm | Roshni Padate, Aamna Patel | 2020 | The paper recommends AES over DES for image security due to AES's higher encryption quality and real-time efficiency. 2. AES is favored over DES in the paper for image security, as it offers superior encryption quality and real-time encryption performance.
3 | Review on Image Encryption/Decryption using AES Algorithm for Hardware Accelerator Design and Implementation | Deeksha P1 , Suchitra M2 , Mokshith B3 , Sharath Kumar K4 , Ayaz Jaffar5 | 2020 | 1. The paper explores AES for hardware-accelerated image encryption, proposing a hybrid approach and discussing challenges like permutation and steganography. 2. It aims to enhance image privacy through improved encryption techniques and hardware acceleration, highlighting the benefits of the AES algorithm.
LITERATURE SURVEY

## Slide 10: CONT…..
S.NO | JOURNAL TITLE | AUTHOR | YEAR | DISCUSSIONS
4 | Implementation of AES Algorithm Using Verilog | Ganesh Gopal Shet , Jamuna V, Shravani S, Nayana H G, Pramod Kumar S | 2020 | 1.Cryptography is crucial for data security, especially with the rise of e-commerce and internet applications, making AES encryption in Verilog essential. 2. AES, with key lengths of 128, 192, and 256 bits, is implemented to protect electronics data, reducing encryption delay through parallel design.
5 | Analysis of AES and DES Algorithm | Elhadi Kenane, Messaoud Garah, Fadila Benmeddour | 2020 | Cryptography encodes data for secure transmission; AES and DES are popular algorithms studied here for efficiency and security parameters. 2. The paper explores cryptographic algorithms like AES and DES, analyzing their efficiency based on time, bit independence, and avalanche effect.
6 | Implementation of Data Encryption Standard algorithm using Verilog | Ashwini.R.Patil , Pramod Patil , Rajeshwari. Khot, Laxmi Patil, Anusha Fernandes | 2018 | 1. DES is a symmetric key algorithm encrypting data in 64-bit blocks using a 56-bit key, employing substitution and permutation techniques. 2. It encrypts and decrypts using the same key, processing data in 64-bit blocks with a 56-bit key length.

## Slide 11
S.NO | JOURNAL NAME | AUTHORS | YEAR | DISCUSSIONS
7 | Image Encryption and Decryption using AES | Manoj. B, Manjula N Harihar | 2019 | 1. The document implements AES for image encryption and decryption in communication systems, highlighting its efficiency in software and hardware. 2. It emphasizes data security, detailing AES's symmetric cryptography in rounds, with FPGA implementation using VHDL.
8 | FPGA Implementation of AES for Image Encryption and Decryption | Vijayakumar P, Chaitanya Kumar Chittoju, A.V.Bharadwaja, Payal P. Tayade, Tamilselvi M, R.Rajashree, Xiao-Zhi Gao | 2019 | 1. The document examines FPGA implementation of AES for 128-bit image encryption, with a proposed S-Box structure. 2. It involves MATLAB for image data conversion, simulation with Model Sim-Altera 6.4a and Xilinx ISE, focusing on FPGA-based AES encryption.
9 | 2D Image Encryption and Decryption using AES algorithm in spartan – 3E FPGA | handrasekhar V1 , Ravi Babu T2 , PSN Bhaskar3 , Nihar Ranjan Panda4 | 2019 | 1.The paper implements AES 128-bit core on Spartan-3E FPGA for 2D image encryption, utilizing UART for data transfer. 2. It discusses AES specifics, FPGA blocks, and performance analysis, offering secure data transmission solutions for different sectors.
CONT…..

## Slide 12
MATLAB
AES CORE
FPGA
KEYBOARD
MATLAB
IMAGE
ORIGINAL IMAGE
EXISTING SYSTEM
Read the image
1024^1024
encryption
& decryption in Verilog code
decrypted data
supports for both hardware and software system
symmetric key(secret key), same key used in both transmitter and receiver side.
When key matches at the receiver side the output can be on FPGA and these values are displayed on LCD.
used to input the key that is symmetric key.

## Slide 13
CHALLENGES IN EXISTING SYSTEM
The challenges are :
Ensuring the security of digital images during transmission and storage to protect important data and image communication.
Preventing unauthorized access to confidential image data through effective encryption and decryption methods.
Developing Verilog code to implement AES for image encryption and decryption.
Synthesizing and simulating the AES algorithm on the FPGA family of Spartan-6 using Xilinx ISE 12.4 tool.
Achieving a high maximum frequency of 165.462MHz and a throughput of 252.132Mbit/sec for image encryption and decryption.
Ensuring that the implementation is secure against side-channel attacks and other vulnerabilities is
critical for cryptographic algorithms like AES and DES.

## Slide 14
PROPOSED SYSTEM

## Slide 15
SOFTWARE REQUIRED
XILINX ISE TOOL 14.7
PYTHON

## Slide 16
MODULE DESCRIPTION
MODULE 1 - INPUT IMAGE
MODULE 2 – AES CORE ALGORITHM
MODULE 3 - ELECTRONIC CODE BOOK MODE (ECB)
MODULE 4- CIPHER BLOCK CHAINING MODE (CBC)
MODULE 5 - CIPHER FEEDBACK MODE (CFB)
MODULE 6 - OUTPUT FEEDBACK MODE (OFB)
MODULE 7 - OUTPUT IMAGE

## Slide 17
INPUT IMAGE
The input image is in the form of 1024^1024 gray scale image
Each image pixel value between 0 to 255 both encryption and decryption scheme for modes of operation on Advanced Encryption Standard Algorithm.
Using python NUMPY and CV2 package to convert the (fig 2.) into the Binary text and vice versa.
MODULE 1:

## Slide 18
CONT….

## Slide 19
Symmetric Block Cipher
Known as the Rijndael algorithm.
Block size: 128 bits.
Key sizes: 128, 192, and 256 bits.
Process:
Encrypts data in 128-bit blocks.
Joins encrypted blocks to form ciphertext.
Structure:
Based on a Substitution-Permutation Network (SP network).
Substitutions: Replace inputs with specific outputs.
Permutations: Bit shuffling operations.
What is the Advanced Encryption Standard?
MODULE 2:

## Slide 20
SP Network: It works on an SP network structure rather than a Feistel cipher structure, as seen in the case of the DES algorithm.
Key Expansion: It takes a single key up during the first stage, which is later expanded to multiple keys used in individual rounds.
Byte Data: The AES encryption algorithm does operations on byte data instead of bit data. So it treats the 128-bit block size as 16 bytes during the encryption procedure.
Key Length: The number of rounds to be carried out depends on the length of the key being used to encrypt data. The 128-bit key size has ten rounds, the 192-bit key size has 12 rounds, and the 256-bit key size has 14 rounds.
What are the Features of AES?

## Slide 21
How Does AES Work?
Data Transmission:
AES operates on a 4x4 matrix (state array) where each cell holds 1 byte (16 bytes total per block).
State Array:
The 4x4 matrix holds the data for a single 128-bit block.
Key Expansion:
Initial key is expanded into multiple round keys.
For a 128-bit key: 10 rounds + 1 initial key = 11 keys total.
Round Keys:
Used in each step of the encryption process.

## Slide 22
STEPS TO BE FOLLOWED IN AES

## Slide 23
The mentioned steps are followed for each block sequentially, and the encrypted blocks are combined to form the final ciphertext. Steps include SubBytes, ShiftRows, MixColumns, and Add Round Key.
CONT….
Add Round Key: You pass the block data stored in the state array through an XOR function with the first key generated (K0). It passes the resultant state array on as input to the next step.

## Slide 24
CONT….
Sub-Bytes: In this step, it converts each byte of the state array into hexadecimal, divided into two equal parts. These parts are the rows and columns, mapped with a substitution box (S-Box) to generate new values for the final state array.

## Slide 25
CONT….
Shift Rows: It swaps the row elements among each other. It skips the first row. It shifts the elements in the second row, one position to the left. It also shifts the elements from the third row two consecutive positions to the left, and it shifts the last row three positions to the left.

## Slide 26
CONT….
Mix Columns: It multiplies a constant matrix with each column in the state array to get a new column for the subsequent state array. Once all the columns are multiplied with the same constant matrix, you get your state array for the next step. This particular step is not to be done in the last round.

## Slide 27
CONT….
Add Round Key: The respective key for the round is XOR ’ d with the state array is obtained in the previous step. If this is the last round, the resultant state array becomes the ciphertext for the specific block; else, it passes as the new state array input for the next round.

## Slide 28
CONT….
Now that you grasp the fundamental steps of the encryption process, consider this example to follow along.

## Slide 29
CONT….
In the image above, both the plaintext and encryption keys are converted to hex format before beginning the operations. You can then generate the keys for the next ten rounds, as shown below.

## Slide 30
CONT….
Follow the same steps as explained above, sequentially extracting the state array and using it as input for the next round. The steps are as follows:
Add Round Key:

## Slide 31
CONT….
Sub-Bytes: It passes the elements through a 16x16 S-Box to get a completely new state array.

## Slide 32
CONT….
Shift Rows:

## Slide 33
CONT….
Mix Columns:

## Slide 34
CONT….
Add Round Key:

## Slide 35
This state array is now the final ciphertext for this particular round. This becomes the input for the next round. Depending on the key length, you repeat the above steps until you complete round 10, after which you receive the final ciphertext.
CONT….

## Slide 36
CONT….
Applications of AES:
Wireless Security: Used in WiFi networks for authentication.
Encrypted Browsing: Ensures secure SSL/TLS encryption for website communication.
General File Encryption: Encrypts files for secure transfer
Processor Security: Some processors use AES for hardware-level encryption.

## Slide 37
CONT….
Differences Between AES & DES
AES is a more secure and efficient encryption standard compared to DES. AES provides better protection against attacks and is widely used in various applications where data security is paramount.

## Slide 38
It is easier because of direct encryption of each block of input plaintext and output is in form of blocks of encrypted ciphertext.
Generally, if a message is larger than b bits in size, it can be broken down into a bunch of blocks and the procedure is repeated.
Advantages of ECB
Parallel encryption of blocks of bits is possible, thus it is a faster way of encryption.
Disadvantages of ECB
Prone to cryptanalysis since there is a direct relationship between plaintext and ciphertext.
ELECTRONIC CODE BOOK MODE (ECB)
MODULE 3:

## Slide 39
Block Diagram for Electronic code book mode
P1
ENCRYPTION
C2
P2
C2
ENCRYPTION
………
………
Pn
ENCRYP
TION
Cn
K
K
K
C1
DECRYPTION
P1
C2
DECRYP
TION
P2
………
………
K
K
K
Cn
DECRYP
TION
Pn
Encryption:
Decryption:
K- KEY
P-PLAIN TEXT
C-CIPHER TEXT

## Slide 40
ENCRYPTED IMAGE:
DECRYPTED IMAGE:
1024 x 1024

## Slide 41
RTL SCHEMATIC DIAGRAM FOR ENCRYPTION

## Slide 42: Electronic Code book Mode (ECB) - Encryption SIMULATION

## Slide 43
RTL SCHEMATIC DIAGRAM FOR DECRYPTION

## Slide 44
Electronic Code book Mode (ECB) - Decryption SIMULATION

## Slide 45
In CBC, the previous cipher block is given as input to the next encryption algorithm after XOR with the original plaintext block.
In a nutshell here, a cipher block is produced by encrypting an XOR output of the previous cipher block and present plaintext block.
CIPHER BLOCK CHAINING MODE (CBC)
Advantages of CBC
CBC works well for input greater than b bits.
Good authentication mechanism.
Better resistive nature towards cryptanalysis than ECB.
Disadvantages of CBC
Parallel encryption is not possible since every encryption requires a previous cipher
MODULE 4:

## Slide 46
Block Diagram For Cipher Block Chaining Mode
…….
……
P1
+
IV
K
Encryption
C1
P2
+
K
Encryption
C2
Pn
+
K
Encryption
Cn
Initialisation Vector- (IV)
Plain text – P
Key – k
Cipher text - C

## Slide 47
ENCRYPTED IMAGE
DECRYPTED IMAGE
1024 x 1024

## Slide 48
RTL SCHEMATIC DIAGRAM FOR ENCRYPTION AND DECRYPTION

## Slide 49: CIPHER BLOCK CHAINING MODE (CBC)-Encryption and Decryption SIMULATION

## Slide 50
In this cipher feedback (CFB) mode, an initial vector (IV) is used for the first encryption. Output bits are divided into sets of 's' and 'b-s' bits.
's' bits are XORed with plaintext, then inputted into a shift register. Encryption and decryption follow similar procedures using encryption algorithms.
CIPHER FEEDBACK MODE (CFB)
Advantages of CFB
Since, there is some data loss due to the use of shift register, thus it is difficult for applying cryptanalysis.
Disadvantages of using CFB
lacking block loss support and concurrent encryption, but allows loss-tolerant, parallelizable decryption..
MODULE 5:

## Slide 51
Block Diagram For Cipher Feedback Mode
IV
K
Encryption
s bits
b-s bits
C1
P1
Shift register
b-s bits s bits
K
Encryption
s
bits
b-s bits
C2
P2
……..
…….
Shift register
b-s bits s bits
Encryption
K
s
bits
b-s
bits
Cn
Pn
Encryption and Decryption
Initialisation Vector- (IV)
Plain text – P
Key – k
Cipher text – C

## Slide 52
ENCRYPTED IMAGE
DECRYPTED IMAGE
1024 x 1024

## Slide 53
RTL SCHEMATIC DIAGRAM FOR ENCRYPTION

## Slide 54: CIPHER FEEDBACK MODE (CFB) - Encryption SIMULATION

## Slide 55
RTL SCHEMATIC DIAGRAM FOR DECRYPTION

## Slide 56: CIPHER FEEDBACK MODE (CFB) - Decryption SIMULATION

## Slide 57
Output Feedback Mode (OFB) operates similarly to Cipher Feedback Mode (CFB) but transmits encrypted output rather than the cipher itself.
Unlike CFB, it sends all block bits, enhancing error resistance and reducing cipher dependency on plaintext, offering robust transmission and security.
OUTPUT FEEDBACK MODE (OFB)
Advantages of OFB
OFB prevents error propagation unlike CFB, ensuring plaintext block integrity.
Disadvantages of OFB
The drawback of OFB is that, because to its operational modes, it is more susceptible to a message stream modification attack than CFB.
MODULE 6:

## Slide 58
Block Diagram For Output Feedback Mode
IV
Encryption
K
P1
C1
K
Encryption
P2
C2
……..
Encryption
Pn
…….
Cn
K
Encryption and Decryption
Initialisation Vector- (IV)
Plain text – P
Key – k
Cipher text – C

## Slide 59
ENCRYPTED IMAGE
DECRYPTED IMAGE
1024 x 1024

## Slide 60
RTL SCHEMATIC DIAGRAM FOR ENCRYPTION

## Slide 61: OUTPUT FEEDBACK MODE (OFB)- Encryption SIMULATION

## Slide 62
RTL SCHEMATIC DIAGRAM FOR DECRYPTION

## Slide 63: OUTPUT FEEDBACK MODE (OFB)- Decryption SIMULATION

## Slide 64
OUTPUT IMAGE
MODULE : 7

## Slide 65
DESIGN SUMMARY
1.POWER
Explore AES and DES algorithms power consumption.
Focus on resource-constrained environments (mobile, IoT).
Minimize energy usage.
Study algorithmic complexities.
Analyze implementation strategies.
The existing system consumed the total power as 28117.452nw And the proposed system consumed the total power as 28007.383.MHz.

## Slide 66
Power consumption metric

## Slide 67
2.AREA
Area Summary in Xilinx Design Suite.
In-depth FPGA resource utilization analysis.
Breakdown of logic cells, flip-flops, block RAMs, LUTs.
Optimize resource allocation.
Improve design efficiency.

## Slide 68
AREA UTILIZATION

## Slide 69
3.TIME
Timing Summary in Xilinx Design Suite.
Detailed FPGA timing analysis.
Critical path, setup/hold times, max frequency.
Ensure timing requirements.
Optimize timing closure, performance.

## Slide 70
Design timing summary

## Slide 71
CONCLUSION
AES algorithm when implemented is among the best encryption and decryption standards in modes of operation such as ECB, CBC, CFB, OFB. This work presents the concept and implementation of Image Encryption and Decryption using AES-128 bit to safeguard sensitive image data from unauthorized access.
It is beneficial to investigate the route for putting such an approach into practice utilizing Verilog code that is generated and simulated with the ISE in the Xilinx Family Kintex-7.The Maximum Frequency achieved from the design is 100MHz and the power consumption rate is 28007.343nw for the Image Encryption and Decryption.

## Slide 72
Performance Optimization: Enhance encryption and decryption speed to achieve higher throughput and lower latency.
Scalability Improvements: Adapt the system for larger datasets and more complex image processing tasks.
Key Management: Integrate robust key management mechanisms to enhance security.
Additional Security Features: Implement authentication and tamper resistance to further secure encrypted data.
Wider FPGA Compatibility: Extend the implementation to other FPGA families beyond Kintex-7 for broader applicability.
Future Scope

## Slide 73
REFERENCES
[1] Perspectives in Communication, Embedded-Systems and Signal-Processing (PiCES) – An International Journal ISSN: 2566-932X, Vol. 2, Issue 11, February 2019 © ΠCES 2018. All right reserved. Publisher: PiCES Journal, www.pices-journal.com 342 AES Based Algorithm for Image Encryption and Decryption.
[2] IMAGE ENCRYPTION AND DECRYPTION USING AES ALGORITHM Roshni Padate1, Aamna Patel2. ISSN 0976 – 6464(Print) ISSN 0976 – 6472(Online) Volume 6, Issue 1, January (2015), pp. 23-29 http://www.iaeme.com/IJECET.asp Journal Impact Factor (2014): 7.2836 www.jifactor.com,INTERNATIONAL JOURNAL OF ELECTRONICS AND COMMUNICATION ENGINEERING & TECHNOLOGY (IJECET)

## Slide 74
CONT…
[3] Review on Image Encryption/Decryption using AES Algorithm for Hardware Accelerator Design and Implementation IOSR Journal of VLSI and Signal Processing (IOSR-JVSP) Volume 10, Issue 4, Ser. I (Jul. - Aug. 2020), PP 08-19 e-ISSN: 2319 – 4200, p-ISSN,No:2319–4197 www.iosrjournals.org Deeksha P1 , Suchitra M2 , Mokshith B3 , Sharath Kumar K4 , Ayaz Jaffar5
[4] Image Encryption and Decryption using AES International Journal of Engineering and Advanced Technology (IJEAT) ISSN: 2249-8958 (Online), Volume-1 Issue-5, June 2012 Manoj. B, Manjula N Harihar

## Slide 75
CONT…
[5] FPGA Implementation of AES for Image Encryption and Decryption International Journal of Innovative Technology and Exploring Engineering (IJITEE) ISSN: 2278-3075, Volume-8 Issue-7 May, 2019 Vijayakumar P, Chaitanya Kumar Chittoju, A.V. Bharadwaja, Payal P. Tayade, Tamilselvi M, R. Rajashree, Xiao-Zhi Gao
[6] 2D IMAGE ENCRYPTION AND DECRYPTION USING AES ALGORITHM IN SPARTAN - 3E FPGA Chandrasekhar V1 , Ravi Babu T2 , PSN Bhaskar3 , Nihar Ranjan Panda4 M. Tech Student, Assistant professor, Assistant professor, Associate professor Dept. of Electronics &Communication Engineering, Sanketika Vidya Parishad Engineering College, Visakhapatnam, India